## Slide 1: Smart Home Intercom System
Prepared for:
D. Kevin McGrath
Prepared by:
Glen Anderson
Jordan Davis
Lazar Sharipoff

## Slide 2: Purpose:
Replace old fashioned paging systems
Remove the need to shout throughout the house
Ability to page a specific node
  Ability to identify rooms with a person in them and page to these rooms
Ability to have a video conversation in separate rooms

## Slide 3: Requirements:
Place call from one node to another
  Call can stream audio and video
Secure
  Audio and video encrypted
  No audio or video data is stored, only streamed
  No connection to external network
  Different user modes with varying levels of access
Ability to detect a person in a room
Reasonably easy setup, minimal configuration
Low per unit cost
  ~$200.00

## Slide 4: Systems:
Hardware
Operating System
Software
Screen
Audio I/O
Networking
Data Storage
Encryption
Person Detection
IR Camera
Raspberry Pi 3

## Slide 5: Hardware:
Raspberry Pi 3
Touchscreen
Case
Audio Hat
Microphone
IR Camera

## Slide 6: Raspberry Pi 3
Small single board computer
Fits within budget
Can be deployed with software package pre-installed
Can support multiple sensors and pieces of hardware
Has a large amount of community support

## Slide 7: Touchscreen
7” Screen
  Size and Resolution
  Cost

## Slide 8: Case
Case
  Can house a 7” touch screen
  Can be mounted on wall
  Keeps USB ports of Pi open
  Can have camera mounted to it easily
  Supports expansion
    GPIO pins for hats
    Punch out hole for heatsink

## Slide 9: Camera
NoIR Camera
  Will be upgraded to IR
  Used for video stream input
  Used for person detection

## Slide 10: Audio I/O
HiFiBerry sound card for audio output
  Higher quality than built in sound card
  Widely available
Sparkfun microphone or USB microphone for audio input
  USB microphone would require no hardware configuration but would allow for less flexibility
  Sparkfun microphone would have to be installed, but would allow for flexibility with the design of each node
VideoLAN media player to stream audio between nodes
  Compatible with the platform

## Slide 11: Operating System
OS will be implemented using Raspbian Stretch
  Two options available, Stretch and Stretch Lite
  Stretch Lite is implemented without a GUI
  Stretch has GUI but is approximately 1.25GB larger
  Ultimately as a proof of concept, Stretch will have greater support of systems.

## Slide 12: Software:
Network Modules
Network Encryption
Person Detection
Data Management
Video Streaming Software
User Interface

## Slide 13: Network Modules
Qt 4.8 Network Module
  Examples online to test implementation
  Encapsulates application data
Better Approach to Mobile AdHoc Networking (B.A.T.M.A.N.)
  Batman-adv is a well documented implementation
  Layer 2 implementation
  Will be using WPA_NONE for encryption
  Will create its own mesh network for talking between nodes

## Slide 14: Person Detection
IR-capable camera
  Use for initial detection of a person entering a room to bring the system out of sleep mode
Facial recognition
  Use OpenCV library for facial recognition
  Used to verify that the IR system detected an actual person
  Log that a person is in the room so that other devices can use this information when suggesting which room to call

## Slide 15: Data Management
Flat file system for storing data
  Store which room last had a person in it
  Log detailed errors for troubleshooting purposes
Need to reliably check which rooms had a person in them
  Files will be read directly from related programs, which will be activated when the system powers on

## Slide 16: Video Streaming Software
VLC
  Capture Rate
    Can be set to the max capture rate of the installed camera
  Hardware Compatibility
  Bandwidth
  Can stream audio
  Installation

## Slide 17: User Interface:
Implemented using Qt 4.8
Will boot using embedded mode straight into the program
Will first be implemented as a baseline to test network connectivity and video capture
Ultimately should be able to control brightness and contrast along with controlling camera power and swapping user modes

## Slide 18: Where we are
Alpha level functionality of individual components
Video streaming working as proof of concept over UDP using gstreamer
Home screen designed with QT 4.8
Facial detection using OpenCV working

## Slide 19: Changes from the plan
Qt 5.0 embedded mode requires a subscription
Qt 4.8 has embedded mode and is well supported freeware.
VLC is difficult to set up in embedded mode, so gStreamer will be used to stream video instead

## Slide 20: Video streaming
Streaming between two nodes
  High latency, receiver overheats
gstreamer instead of VLC
  Embedded mode better supported with gstreamer
Possible solutions
  Use raw video instead of H264, which will help with FPS and latency issues
  Use heatsink and/or fan on back of the Raspberry Pi
  Use an UPboard as transmitting node if streaming is still slow

## Slide 23: User interface
Home screen
  In progress, still needs to be tested on the Raspberry Pi
Options menu
  In progress, design done but needs to be implemented
Status bar
  In progress, design done but needs to be implemented

## Slide 25: Person detection
            OpenCV implemented, need to add infrared sensing
            May have to adjust colors when using infrared cameras as they could distort colors when playing video
            Need to compile face detection on the Raspberry Pi

## Slide 27: Person detection script (using OpenCV)
Based on this resource: https://realpython.com/blog/python/face-detection-in-python-using-a-webcam/

## Slide 28: Problems
Scheduling difficulties continue to be an issue
  To overcome scheduling difficulties, establish consistent meeting times and cancel as far ahead in advance as possible (if needed)
Video streaming has low quality and high latency
  This is likely due to the overhead of encoding and decoding the video, we will troubleshoot by streaming raw video at a lower resolution
When streaming video, receiving node overheats
  We will use a heat sink and possibly a fan to cool off the system, and remove some of the overhead with encoding video
Libraries like OpenCV take up a lot of space and will require a substantial portion of the available computing resources, this may become an issue eventually

## Slide 29: What needs to get done
BATMAN needs to be implemented for the mesh network
User interface needs to be finished and back-end needs to be added
Person detection needs to be updated to include infrared sensing to tell a person apart from a pet
Video streaming needs to be enhanced so that it is fast
Audio I/O hardware needs to be added and audio streaming needs to be implemented

## Slide 30: Implementation sequence (updated from Fall report)
Operating System
User Interface
Assembling Hardware
Encryption
Person Detection
Video Streaming
B.A.T.M.A.N.
Audio Streaming
Data Storage
1
5
4
3
2

## Slide 31: Conclusion
Comfortable with where we are, certain components need to be worked on more in depth than others like batman-adv and audio streaming
Will continue meeting together on weekends to work more as a group
Looking forward to having a working product that can be prepackaged with a user manual